## Slide 1: x86 Assembly Part 1

## Slide 2: Register Naming
How many general purpose register names are there for 64-bit, 32-bit, 16-bit and 8-bit, respectively?

## Slide 3: Register Naming
64-bit (total 16)
  %r[a-d]x, %rdi, %rsi, %rsp, %rbp, %r[8-15]
32-bit (total 16)
  %e[a-d]x, %edi, %esi, %esp, %ebp, %r[8-15]d
16-bit (total 16)
  %[a-d]x, %di, %si, %sp, %bp, %r[8-15]w
8-bit (total 20)
  %[a-d][lh], %dil, %sil, %spl, %bpl, %r[8-15]b

## Slide 4: Register Functionality
What is the functionality each register poses?

## Slide 5: Register Functionality
%?ax – Accumulator
%?bx – Base
%?cx – Counter
%?dx – Data
%?di – Destination Indicator
%?si – Source Indicator
%?sp – Stack Pointer
%?bp – Base Pointer

## Slide 6: Register Functionality
x86 is CISC. To give you a taste, see an alternative implementation of memcpy, called blkcpy (block copy).
Will come back in the next seminar, after you are acquainted with procedure calls.

## Slide 7: Register Functionality
#include <stdio.h>
#include <string.h>
void blkcpy(void *tgt,
const void *src, size_t len);
char ibuff[1 << 10], obuff[1 << 10];
int main() {
fgets(ibuff, 1 << 10, stdin);
blkcpy(obuff, ibuff, strlen(ibuff));
printf("%s", obuff);
return 0;
}
blkcpy:
movq %rdx, %rcx
cld
rep movsb
ret

## Slide 8: Challenge Question 0
How many (conditional) jumps are needed to implement the following semantic?
If -3 < x < 20, call foo()

## Slide 9: Challenge Question 0
Only ONE conditional jump is needed.
addq $2, %edx
cmp $22, %edx
jae skip
call foo
skip:
…

## Slide 10: Challenge Question 1
What is the semantic of the following assembly?

## Slide 11: Challenge Question 1
00: mov %edi,%eax
02: mov $0x2aaaaaab,%edx
07: sar $0x1f,%edi
0a: imul %edx
0c: mov %edx,%eax
0e: sub %edi,%eax
10: retq
int div6(int x)
{
return x / 6;
}

## Slide 12: Challenge Question 2
What is the difference of instruction inc compared to other arithmetic instructions?
And why?

## Slide 13: Challenge Question 2
CF (carry flag) is promised not to be modified after the instruction.
Provide a neat way to implement large integer.

## Slide 14: Challenge Question 3
What are the two ways of translation of while block to assembly?
And why that?

## Slide 15: Challenge Question 3
void bar();
void foo(int cnt)
{
while (cnt > 0)
{
bar();
--cnt;
}
}
00: push %rbx
01: mov %edi,%ebx
03: jmp 12 <foo+0x12>
05: mov $0x0,%eax
0a: callq ??? <bar>
0f: sub $0x1,%ebx
12: test %ebx,%ebx
14: jg 5 <foo+0x5>
16: pop %rbx
17: retq
jump to middle (-Og)

## Slide 16: Challenge Question 3
void bar();
void foo(int cnt)
{
while (cnt > 0)
{
bar();
--cnt;
}
}
00: push %rbx
01: mov %edi,%ebx
03: jmp 12 <foo+0x12>
05: mov $0x0,%eax
0a: callq ??? <bar>
0f: sub $0x1,%ebx
12: test %ebx,%ebx
14: jg 5 <foo+0x5>
16: pop %rbx
17: retq
jump to middle (-Og)

## Slide 17: Challenge Question 3
void bar();
void foo(int cnt)
{
while (cnt > 0)
{
bar();
--cnt;
}
}
00: push %rbx
01: mov %edi,%ebx
03: test %edi,%edi
05: jle 16 <foo+0x16>
07: mov $0x0,%eax
0c: callq ??? <bar>
11: sub $0x1,%ebx
14: jne 7 <foo+0x7>
16: pop %rbx
17: retq
guarded do while (-O1 -O2 -O3)

## Slide 18: That’s all.