## Slide 1: x86 Assembly Part 2

## Slide 2: Challenge Question 0
Why sometimes %rdx is used for passing function return value?

## Slide 3: Challenge Question 1
00: pxor %xmm0,%xmm0
04: cvtsi2sd %esi,%xmm0
08: mulsd Const(%rip),%xmm0
10: movsd %xmm0,(%rdi)
14: retq
0x600807 | 40
0x600806 | 19
0x600805 | 1e
0x600804 | b8
0x600803 | 51
0x600802 | eb
0x600801 | 85
0x600800 | 1f
Const + %rip

## Slide 4: SSE Instruction Set
SSE Register
  x86 %xmm0 – %xmm7
  x86-64 %xmm0 – %xmm15
128 bits each
Each contains
  4 float, or 2 double
  or 4 int, or 2 long long
Can operate multiple arithmetic.

## Slide 5: SSE SIMD Operation
Single Instruction Multiple Data
Parallel computation with a single instruction
addpd %xmm1, %xmm0 // add packed double
%xmm1
%xmm0
double 3
double 2
double 1
double 0
+
+
%xmm0
double 5
double 4
=
=

## Slide 6: Basic Floating Point Arithmetic
Only use the low order bits of SSE registers
addsd %xmm1, %xmm0 // add scalar double
%xmm1
%xmm0
double 3
double 2
double 1
double 0
+
+
%xmm0
double 1
double 4
=
=

## Slide 7: Basic Floating Point Arithmetic
float + float
  addss %xmm1, %xmm0 // add scalar single
double + double
  addsd %xmm1, %xmm0 // add scalar double
double – double
  subsd %xmm1, %xmm0 // subtract scalar double
double * double
  mulsd %xmm1, %xmm0 // multiply scalar double
double / double
  divsd %xmm1, %xmm0 // divide scalar double

## Slide 8: Type Conversion & Load Store
int to double
cvtsi2sd %eax, %xmm0
// convert scalar int to scalar double
Move a double
movsd %xmm0,(%rdi)
// move scalar double

## Slide 9: Type Conversion & Load Store
Move several double
movapd %xmm0, %xmm1
// move aligned packed double

## Slide 10: Calling Convention (x86-64)
Floating point arguments are passed in %xmm0 - %xmm7
On stack if there are more
Return value is in %xmm0
All %xmm registers are caller saved

## Slide 11: More Bits in YMM, ZMM
Streaming SIMD Extensions (SSE, SSE2, SSE3, SSE4.1, SSE4.2)
  128-bit %xmm
Advanced Vector Instruction (AVX, AVX2)
  256-bit %ymm
  vaddsd, vsubsd, vmulsd, vdivsd…
AVX256
  512-bit %zmm

## Slide 12: AVX SIMD Operation
vaddpd %ymm1, %ymm0, %ymm0
// add packed double
%ymm1
%ymm0
double 1
%ymm0
double 0
double 2
double 3
double 5
double 4
double 6
double 7
double 9
double 8
double a
double b
+
+
+
+
=
=
=
=

## Slide 13: Challenge Question 1 Comes Back
00: pxor %xmm0,%xmm0
04: cvtsi2sd %esi,%xmm0
08: mulsd Const(%rip),%xmm0
10: movsd %xmm0,(%rdi)
14: retq
0x600807 | 40
0x600806 | 19
0x600805 | 1e
0x600804 | b8
0x600803 | 51
0x600802 | eb
0x600801 | 85
0x600800 | 1f
Const + %rip

## Slide 14: Challenge Question 1 Comes Back
00: pxor %xmm0,%xmm0
04: cvtsi2sd %esi,%xmm0
08: mulsd Const(%rip),%xmm0
10: movsd %xmm0,(%rdi)
14: retq
Const + %rip 0x40191eb851eb851f
void func(double *dest,
int r)
{
*dest = 6.28 * r;
}

## Slide 15: Challenge Question 2
00: movswl 0x4(%esp),%eax
05: add 0xc(%esp),%eax
09: movswl 0x8(%esp),%edx
0e: add 0x10(%esp),%edx
12: mov 0x14(%esp),%ecx
16: sub 0x18(%esp),%ecx
1a: imul %ecx,%edx
1d: sub %edx,%eax
1f: ret
int cal_6(short a, short b,
int c, int d,
int e, int f)
{
return (a + c)
- (b + d)
* (e - f);
}

## Slide 16: Challenge Question 3
Which register is caller-saved or callee-saved under 32bit Linux?

## Slide 17: Challenge Question 3
Caller-Saved:
%eax, %ecx, %edx
Callee-Saved:
%ebx, %edi, %esi, %ebp

## Slide 18: Challenge Question 4
Decode the following assembly.
cal:
enter $8, $0
movl %edi, 4(%rsp)
movl %esi, (%rsp)
movl -4(%rbp), %eax
movl -8(%rbp), %edx
subl %edx, %eax
leave
ret
enter
# pushq %rbp
# movq %rsp, %rbp
# subq $8, %rsp
leave
# movq %rbp, %rsp
# popq %rbp

## Slide 19: That’s all.